## Slide 1
LLDPC: A Low-Density Parity-Check Coding Scheme for LoRa Networks
Kang Yang and Wan Du
﻿Department of Computer Science and Engineering University of California, Merced

## Slide 2: Overview
Smart City[2]
Smart Farming[1]
Wide Area Coverage
Long Battery Life
Low Data Rate
[1] https://iotdesignpro.com/articles/smart-farming-iot-applications-in-agriculture
[2] https://earth.org/smart-city-technologies/

## Slide 3: Overview
LoRa Primer
Forward Error Correction (FEC) Encoding
Payload Bits: 1 1 0 1
Chirp Spread Spectrum (CSS) Modulation
1 1 0 1 1 0 0
CSS Demodulation
FEC Decoding
0 1 0 1 1 0 0
Payload Bits: 1 1 0 1
Sender
Receiver
Channel

## Slide 4: Motivation
Hamming Codes – Limited Error Correction Capacity
Can we develop a more efficient error correction code for LoRa?
PRR (Packet Reception Ratio) and BRR (Bit Reception Ratio)
Low PRR but high BRR, indicating a small number of erroneous bits.

## Slide 5: Motivation
Low-Density Parity-Check (LDPC) Codes[4]
Capacity-Achieving: Supports data rates close to the Shannon limit in Gaussian channels
Popularity: 5G-NR, DVB-S/S2, 802.11, Near-Earth, Deep space
​ Light-Weight Encoding: Same as Hamming codes, only XOR operation
[4] Srikar Kasi and Kyle Jamieson. Towards quantum belief propagation for LDPC decoding in wireless networks. In ACM MobiCom, 2020.

## Slide 6: Design of LLDPC
LLDPC
Integrating LDPC Codes into LoRa

## Slide 7: LDPC Codes Primer
Encoding - XOR Operation
b1 | b2 | b3 | b4 | b5 | b6 | b7 | b8 | b9 | b10
1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
Payload bits:
Encoded bits:
Parity-check matrix H

## Slide 8: LDPC Codes Primer
b1 | b2 | b3 | b4 | b5 | b6 | b7 | b8 | b9 | b10
1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
Parity-Check Matrix H =
Decoding – Soft Belief Propagation (SBP) Algorithm
Factor nodes
Variable nodes
b
b
b
Factor
Graph

## Slide 9
Decoding – SBP Algorithm
Demodulation
LDPC Decoding by the SBP Algorithm
Receiver
b1 | b2 | b3 | b4 | b5 | b6 | b7 | b8 | b9 | b10
-0.6 | -0.8 | -0.7 | -0.1 | 0.1 | 0.9 | -0.7 | 0.6 | -0.5 | 0.5
-0.6 | -0.8 | -0.7 | -0.1 | 0.1 | 0.9 | -0.7 | 0.6 | -0.5 | 0.5
LDPC Codes Primer
Details of SBP in the paper.

## Slide 10: Design of LLDPC
Payload Bits
LoRa CSS Modulation
Encoded Bits
LoRa CSS Demodulation
LDPC Decoding
Payload Bits
Sender
Receiver
Channel
LDPC Encoding by Simple XOR Operation

## Slide 11: Design of LLDPC
Challenge 1 – No LLR for LoRa CSS Demodulation
Time
BW
Down-Chirp
Received Chirp
De-Chirping
1 63 128
Frequency Bin Index
FFT (Fast Fourier Transform)
0 0 1 1 1 1 1 1
No LLR (Log-Likelihood Ratio).
Binary Sequence

## Slide 12: Design of LLDPC
Solution 1 – Amplitude Spectrum-based LLR extractor
Index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
b1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
b2 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
b3 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
Insight: All frequency bins have the impact on the bit value
0 1 2 3 4 5 6 7
Frequency Bin Index
Probability distribution of eight bins in a symbol which contains 3 bits when SF = 3.
SoftMax
The sum of the probabilities of believing b1 = 0
The sum of the probabilities of believing b1 =1

## Slide 13: Design of LLDPC
Challenge 2 – Low Decoding Efficiency
The pre-decoding and post-decoding BER (Bit Error Ratio) before and after LDCP decoding.
Identify erroneous bits to reduce their LLR.
The CDF (Cumulative Distribution Function) of the absolute LLR value for erroneous bits.

## Slide 14: Design of LLDPC
Solution 2 – Symbol-Aware LLR Enhancement Module
Insight: If there are erroneous bits, its symbol is wrongly demodulated
b1 | b1 | b3
0.9 | -0.6 | -0.3
0.9p | -0.6p | -0.3p
0 1 2 3 4 5 6 7
Frequency Bin Index
SoftMax
Amplitude Spectrum-based LLR extractor
Wrongly Demodulated Symbol Detection Model
If the symbol is incorrectly demodulated.
Original LLR
Enhanced LLR
Probability p
Details of symbol detection model in the paper.

## Slide 15: Design of LLDPC
Solution 2 – Symbol-Aware LLR Enhancement Module
The CDF of the absolute LLR for erroneous bits w/o and w/ symbol-level information.

## Slide 16: Design of LLDPC
Challenge 3 – High Decoding Latency
Packet transmission
Receiving window #1
Transmission
Receiving window #2
Delay #1 (1s)
Delay #2 (2s)
There are one or two seconds to reply ACK (Acknowledgement) for receivers.
 | CR=4/5 | CR=4/6 | CR=4/7
Decoding latency | 2.51 s | 3.27 s | 5.46 s
SBP needs a large number of iterative update, which causes long decoding latency
Time consumption of the SBP to decode one packet for different CRs on the Raspberry Pi 3.
Cannot meet the time constraint.
LoRa Node Time Line

## Slide 17: Design of LLDPC
Solution 3 – GNN-based Belief Propagation Algorithm
Insight: If a trained model is available, the Graph Neural Network-based methods[5] require just one inference to output results.
GNN Layer
…
K layers
GNN Layer
Feature Extraction
The LLR of all variable nodes
Classifier Layer
The updated LLR of all bits
1
0
…
0
1
[5] Zhen Zhang, Fan Wu, and Wee Sun Lee. Factor graph neural networks. In NeurIPS, 2020.

## Slide 18: Design of LLDPC
Solution 3 – GNN-based Belief Propagation Algorithm
 | CR=4/5 | CR=4/6 | CR=4/7
GNN-based BP | 0.434 s | 0.628 s | 1.502 s
LLDPC | 0.548 s | 0749 s | 1.871 s
Time consumption of GNN-based BP and LLDPC to decode one packet for different CRs on Raspberry Pi 3.

## Slide 19: Design of LLDPC
Put All Together for LDPC Decoding at Receiver
Received LoRa PHY samples at receiver
LLR
1 | 0 | … | 0 | 1
Spectrum-based LLR extractor
De-chirping
& FFT
Symbol-aware LLR enhancement
GNN-based belief propagation
Enhanced LLR
Amplitude spectrum

## Slide 20: Evaluation
Experiment Setup
  Overall performance
  Ablation study
  Performance under different settings
  Performance on the real dataset

## Slide 21: Evaluation
The In-Field Testbed
USRP N210
LoRa nodes

## Slide 22: Evaluation
Performance in the In-Field Testbed
The BER at ten different locations on a campus-scale testbed.
LLDPC decreases the BER by an average of 57.6% over Hamming.

## Slide 23: Summary
LLDPC, integrating LDPC codes into LoRa.
Three challenges (no LLR, low decoding efficiency, and high decoding latency) and corresponding solutions.
Extensive data-driven experiments.
Code: https://github.com/kangyang73/LLDPC-SenSys22.

## Slide 24
Thank You